## Slide 1: 28P650

## Slide 2: Features
1K fragmented flash 5x128k.
20 Years flash retention at 85deg, 100000 erase cycles at room temp. (10000 at 125deg)
EtherCAT , MCAN built in CPU
Single bit errors are corrected by ECC and logged. Exceeding a threshold may create an interrupt
200MHz PWM
DMA region for CLA (was also in 003x)
Reversed order in running CPUs: CPU1 must be loaded first
ADC double testing
Both register mode and DriverLib are there

## Slide 3: More features
PWM is crazier than ever (e.g. XCMP)
EPG (Embedded pattern generator)
AES (Encription accelerator)
PPB – ADC processor, automatic oversampling and zero cross finding, time stamping actual sample

## Slide 4: Caveat
Peripheral bases (e.g. CAN controller) changed
Peripheral bases need bee considered, E.g. there is PWM crossbar A and B. Also names changes E.g. Crossbar trips changed names to OUTS
Tricky memory management: memories are not ordered as expected
Tricky CLA program memory
Change flash setting in .cmd to ALIGN(64) – They come ALIGN(8)
Re-writing line (adding zeros) without erasure will kill the flash
PREAD loops are inefficient, data within instruction (e.g. MAC) is inefficient

## Slide 5: Fletcher code
Double integral
Detects swaps and cancelling errors

## Slide 6: Flash memory (NA: DCSM OTP, link pointers)
Work flow in API guiide
FlashTech utility – burn with no code composer
All flash configurations must run from RAM , end by 8 NOPs
Only programmable in 64bit (pref. 128) aligned chunks. Preferable 512bit. Use auto ECC (non auto is only for intentional errors in SW checks)
Flash API wholly software
Flash actions only by API
Flash use – semaphoring, wait state setting, bank allocation, pump allocation : user responsibility, use of watchdog, DCSM management (unlocking, or run API callers (not progress checkers!) from same zone).
Recommended – do NOT run interrupts while flash actions executes (no problem if the other CPU runs different flash banks, CLA runs separately from RAM and is not an issue)
API functions exit immediately leaving actions for the FSM. Must wait completion by polling.
PLL must be active
Must flush Fapi_flushPipeline() flash wrapper cache after action completion, before permitting bank use
Never trust the given drivers. E.g. flash semaphore claims block until they get it, may be forever

## Slide 7: Must learn
DCSM (Code Security Module)
DCC (Dual Clock Comparator)